Model: G1WYD-1000

Single-Head Liquid Filling Machine

Operational Manual

Warning：The machines need to Earth Wire, remember!！！

SEMI-AUTOMATIC PISTON FILLING MACHINE

# CLONTENTS

1, Operational Manual

◆ Principle and Property

◆ Specifications

◆ Directions for Safe Operation

◆Instructions for Machine

◆Installation

◆Maintenance

◆Filling Speed

◆Service by our website

◆Fig. 1 and 2

◆Wiring Diagram

◆Troubleshooting

2,Packing List

3, Reception sheet

# Principle and Property

- Principle: The G1WYD series filling machine is semi-automatic and of piston type. The material is pumped by a piston driven by a cylinder. The material flow is controlled by a one-way valve and the cylinder stroke controlled by a reed switch to adjust the filling dosage.

- Performance: The G1WYD series single-headed liquid filling machine is produced on the basis of further transformation and innovation of other type filling machines by introducing advanced foreign technology. Thus its construction is made more simple and more reasonable, accuracy higher, and operation easier. The machine is an ideal selection for your purchasing filling equipment.

##### Specifications

| Technical Parameters | Items | Parameters |
| --- | --- | --- |
|  | Voltage | 220V/110V±5V |
|  | Current | 1A |
|  | Power | 10W |
|  | Rated air pressure | 4-6kg |
|  | Filling Speed | 0-50Bottle/Min. |
|  | Filling Accuracy | ±111 % - ±211 % |
| Filling Results | Model | Filling Range (ml) | Preferred Filling Range （ml） | The model of your machine（√） |
|  | 100 | 5~130 | 10~100 |  |
|  | 280 | 10~330 | 20~280 |  |
|  | 500 | 30~550 | 50~500 |  |
|  | 1000 | 80~1100 | 100~1000 | √ |
|  | 2800 | 350~3100 | 500~2800 |  |
|  | 5000 | 800~5300 | 1000~5000 |  |

#### Directions to Safe Operation

The machine is only suitable for filling low concentration materials such as liquid and cannot be used for other purposes. In order to ensure safe production, please read the following attentions carefully.

- Use air source and power source complying to this machine (Referring to the specifications of this manual).

- Do cut off air source and power source before disassembling and washing this machine.

- Electrical control elements are built in the rear part (close to the control button) of the machine. Do not wash the machine with water at any circs. Otherwise there is a danger of electric shock and damage to control elements.

- A reliable earthing should be ensured by providing a socket with a earthing line.

- Disconnect power from the machine upon repairing the circuit as voltage may exist in the circuit of power control when power is off.

#### Instruction to machine

The machine is an ideal filling machine for the trades of foodstuffs, daily-used chemicals, pesticide, medicine as well as special trades.  In the process of operation, the machine is affected by the following factors:

- The filling accuracy: Compressed air stability, material uniformity  and filling speed

- The filling speed:  material viscosity, cylinder stroke, material tank size, filling nozzle size and operational skill

- The machine is filled by the two methods of pedaling and continuous filling, which can be switched as desired. To keep the workshop neat and avoid the waste of materials, it is suggested to make filling operation by pedaling at the initial stage of your operation if you are not skilled enough.

Installation and Adjustments

- First install the three-way slide valve (11) (See Fig.1) and then material-filling nozzle (14).”(Care should be taken to tighten the clamping band and anchor ear).

- Confirm the reed switch position (The rear reel switch position is fixed. )

- Insert the feed pipe (14) into the charging basket or connect it with the material tank.

- Connect the power source (17) with the machine.

- Connect the air source (19) with the machine.

- Turn on the power supply (22).

- Open the air source (19)(the sliding valve).

- Change the working mode of the switch (04) into “pedaling”

- Tread the pedal switch till a material flows out of the material-filling nozzle(20)

- Turn throttle valve (01) and (06) to adjust the pumping and filling speed properly. To raise working efficiency, adjust the material pumping speed (01)to a higher level and filling speed(06) to a lower level but no material or bubbles coming out of a bottle.

- Measure the filling amount and adjust it to the set value by shifting the reed switch.

- Lock tightly the front reel switch to begin formal filling.

- When your operation becomes skillful, turn your working mode to “Auto”.

Maintenance

1. In order to protect the machine cleaning, do not scrape its surface with a sharp and hard object and wipe its dirt with alcohol.

2. The Cylinder has been lubricated before the product leaves the factory. Do not disassemble the cylinder to append any other lubricant.

3. The one-way valve, three-way stainless steel valve and material tank can be easily disassembled and washed.

Filling Speed

The filling speed is decided by the following five factors:

1. The sucking speed is decided by the viscosity of the material  and the sucking pipe length.

2. The filling speed depends on the caliber of the filling head, the larger caliber will result in faster filling.

3.Foaming speed: Fill a high sudsing product should be  at a slower speed.

4.Filling amount: Fill a large amount at a slower speed.

5.Filling  accuracy: Fill an accurate amount at a slower speed.

Adjustment operation:

Loose the front and rear speed regulation valves (	01)and (06)to adjust the nut.

1. Turn the front unidirectional throttle valve (06) handle clockwise to slow down the cylinder front travel speed and charging speed.

2. Turn the front unidirectional throttle valve (06) handle counterclockwise to accelerate the cylinder front travel speed and charging speed.

3. Turn the rear unidirectional throttle valve (01) handle clockwise to slow down the cylinder withdrawal speed and material-sucking speed.

4. Turn the rear unidirectional throttle valve (01) handle counterclockwise to accelerate the cylinder withdrawal speed and material-sucking speed.

Diagram 1

01. Throttle valve  02. Filter  03. Manometer  04. Selection switch

05. Cylinder  06. Throttle valve  07. Adjustable handle

08. Machine body  09. Changeable nozzle  10. Material cylinder

11. Three-way valve  12. Control valve  13. Bar clasp

14. Material filling nozzle  15. Thin cylinder  16. Transparent steel wire tube

Diagram2

17. Cable connector  18. Fuse holder  19. Air source switch

20. Cable connector (connected to pedal switch )

21. Crawl switch（choose）  22. Power switch  23. Terminals

24. Solenoid (two-position five- way)  25. Silencer

26. Straight way valve  27. coil

Diagram3

AIR CIRCUIT CONTROL DIAGRAM

28. Cylinder for material filling nozzle  29. Cylinder for material pushing

30. Terminal  31. pedal switch  32. Selection switch

33. Fuse  34. Master switch  35. Air source switch  36. Reset switch

Troubleshooting:

| Failures | Elimination |
| --- | --- |
| Cylinder piston refuses to move. | 1．Confirm the power switch(22) is on. |
|  | 2．Confirm the air source switch(19) is on. |
|  | 3．Confirm the fixed reed switch is on. |
|  | 4. Confirm the air pressure shown on the manometer (03) has reached require- ments |
|  | 5. Confirm the piston is not jammed. |
|  | 6. Confirm the material viscosity is proper（The product is used for liquid filling）. |
| Piston dose not return after it comes to the top. | Press the relocation button (21)to adjust fixed reel switch. |
| Filling amount is not accurate or no material feeding. | 1．Confirm that the reed switch position is moved or not. |
|  | 2. Reduce the material-sucking speed of the cylinder (Only for high viscosity material). |
|  | 3. Confirm the one-way valve is not clogged. |
|  | 4. Confirm there is enough material in the charging basket. |
|  | 5．Confirm the joints of the pipes are well sealed. |
| Material leaks from the rear of the material tank. | 1．Check whether the piston ring is broken. If so, make replacement. |
|  | 2．Confirm the piston and the piston rod are firm. |

Packing List

| Model of product：G1WYD Name of product：Semi-automatic piston-type single head liquid filling machine |
| --- |
| Serial No. | Category | Descriptions | Unit | Quan. | Specifica- Tions | Remarks |
| 1 | Technical Document | Main Machine | Set | 1 |  |  |
| 2 |  | Instructions | Copy | 1 |  |  |
| 3 |  | Packing List | Copy | 1 |  |  |
| 4 |  | Receiving Apron | Copy | 1 |  |  |
| 5 |  | Product Certificate | Copy | 1 |  |  |
| 8 | Accessory | Ring | Set | 1 | Model O or XY | Depending on size |
| 9 |  | 3-way valve ring | Set | 1 | Depending on size |  |
| 10 |  | Inner Hexagonal Spanner | Set | 1 | 1.5、2、2.5、3、4、5 |  |
| 11 |  | Screw Driver“+” | Piece | 1 | Ordinary |  |